## Slide 1: Hoarding

## Slide 2
Presentation by:
Sanjay Kumar (Special Officer )
Jamshedpur Notified Area Committee, Jamshedpur, Jharkhand
Jamshedpur
Steel City: a City of Tomorrow
Manhole turned into Machine Hole
(Elimination of Manual Scavenging in Sewer Cleaning)
Since 1st Jan 2021

## Slide 3: CITY BACKGROUND
Population covered- 7.7lakhs (Estimated)
Avg. daily water supply - 80 MLD
Length of Water Mains: - 640 Km
Length of Sewer Lines- 579 Km
4 Sewage Treatment Plant : 64 MLD
10 sewage pumping stations: Automated Operation
20000 Manhole
Total number of SafaiMitras Engaged : 133
Area- 64 Sq Km
No of wards -10
Population (2011)- 6.3 lakhs
Green Cover-37% (Approx)
Road Length:- 713 Km
Chart: 
| households connected to sewerage network: | households connected to on-site sanitation
Sanitation System | 89 | 11
Challenges: The conventional method of sewer cleaning requires manual entry.

## Slide 4
THE GREATER SOCIETAL PROBLEM

## Slide 5
ZERO MANUAL ENTRY
CHALLENGES:
Technical
Safety
Social
THOUGHT:
Design
Mechanization
Social Stigma
IDEAS:
Design Change
Study the application of various cleaning equipment
Create a healthy and safe work environment for all and create a “sense of pride” amongst the workmen involved in cleaning

## Slide 6: Before SafaiMitra Suraksha Challenge
ISSUES /CHALLENGES FACED DURING SEWER LINE DESILTING
Technical problem :
Non-Uniform manhole designs
Unavailability of Approach for cleaning of manholes
Unplanned construction of manholes
One solution(machine) does not address all maintenance requirements
Safety problem:
Sewer line desilting required manual entry
Exposure to poisonous gases inside manholes
Exposure to unhygienic condition leading to health hazard
Depth of manholes were different
Social Problems:
Work Dignity and Self Respect
Item | Depth in Mtr. | Quantity | Cleaning Frequency
Removing Sewer Obstruction |  | 6000 Nos. | Compt. Based
Desilting of Branch Sewer | Up to 2.0 | 213 KM. | Compt. / Requirement Based
Desilting of Main Sewer | >1.5 to 3 | 235 KM. | 2-3 Times/Year
Desilting of Trunk Sewer | >1.5 to 8 | 102 KM. | 
Desilting of Manhole | Up to 1.5 | 12194 Nos. | Compt. / Requirement Based
 | >1.5 to 2.5 | 6779 Nos. | 2-3 Times/Year
 | >2.5 to 8 | 1030 Nos | 

## Slide 7
Process Followed Before SmSC
1. Opening cover
2. Checking Gases
3. Placing Rope Ladder
4.Workmen Entry
5.Workmen Entry
6. Desilting work

## Slide 8
Average Activity Time & Associated Risk
Approx Time line activity for Manhole Cleaning/ Each Manhole |  |  | 
Sr. No. | Activity | Approx. Time in Min | Risk
1 | Opening of Manhole | 1 | Low
2 | Visual Inspection of Man Hole from outside | 1 | Low
3 | Checking of Gas | 1 | Low
4 | Fixing of Entry Ladder | 1 | Low
5 | Entry of Work Men | 1 | Low
6 | Desilting of Manhole (Worker Inside manhole) | 60 | High
7 | Exit of Work Men from Manhole | 1 | Low
8 | Removal of Entry Ladder | 1 | Low
9 | Closing of Manhole | 1 | Low
 | Average Cleaning time/ Each Manhole | 68 | 
Worker has to work in side the Manhole = 60 Min
MH
MH
SEWER PIPE
SILT
SILT

## Slide 9: Oxygen availability inside Manhole (Depth Wise)
The availability of oxygen inside manhole decreases with increase in depth

## Slide 10: Sanitation Infrastructure “Pre-SmSC”
S.No | Name of Maintenance Machine | Number of Vehicles (Nov 2020) | Requirement as per CPHEEO Manual | Number of Vehicles (July 2022)
1. | Combination Hydrovac Equipment | 2 | 3 | 3
2. | Number of Grabbers/Desilting Machines | 2 | 4 | 4
3. | Number of standard de-sludging vehicles | 2 | 2 | 8
4. | Sewer Inspection Camera Apparatus | 6 | 6 | 6
5. | Hydro Jetting Machines | 3 | 5 | 5
6. | Power Bucket machine | 1 | 2 | 2
7. | Power Rodding Apparatus | 16 | 16 | 16
8. | Hydraulic Sewer Root cutters | 1 | 3 | 3

## Slide 11
Sanitation Infrastructure “Present Day”
Super Sucker
Jetting Machine
Jetting Machine
Jetting Machine
Suction cum Jetting Machine
Grabber
Jetting Machine
Suction cum Jetting Machine
Desludging Machine
Desludging Machine

## Slide 12: Manhole to Machine-hole since Jan 2021
Grab Machine
Power Bucket Machine
Suction cum Jetting Machine
Super Sucker Machine
Power Bucket Machine
Super Sucker Machine
Power Bucket Machine

## Slide 13
Deployment of Small Suction and Jetting Machine
Maximum Manhole up to 2 Mtr Situated at back alley or non road area
No approach for big vehicle due to encroachment.
Unsafe condition at non road area for movement of big vehicle.
Demand of customer for mechanized cleaning.
Benefits :-
After deployment of small suction and small jetting machine developed on TATA Intra it is easily reached up to narrow alley / non road area and not required to enter workmen inside manhole for cleaning.
Challenges:
Small Jetting Machine (New)
Small Suction Machine (New)

## Slide 14
HAND MADE EQUIPMENT TO STOP HUMAN ENTRY
Hand Grab for removing Silt/Material
Hand Tools for removing Silt/Material from deep Manhole
Hand Tools for removing
Plastics, Thermos coal
Hand Tools for removing
Plastics, Thermos coal from Sewer

## Slide 15
Activity time after final Implementation
Approx Time line activity for Manhole Cleaning/ Each Manhole` |  |  | 
Sr. No. | Activity | Earlier Activity Time in Min (R0) | Final Activity Time in Min (R2)
1 | Opening of Manhole | 1 | 1*
2 | Visual Inspection of Manhole | 1 | 1*
3 | Checking of Gas | 1 | Not Required
4 | Fixing of Entry Ladder | 1 | Not Required
5 | Entry of Work Men | 1.00 | Not Required
6 | Desilting of Manhole (Worker Inside manhole) | 60 | 0
7 | Exit of Work Men from Manhole | 1 | Not Required
8 | Removal of Entry Ladder | 1 | Not Required
9 | Closing of Manhole | 1 | 1*
 | Average Cleaning time/ Each Manhole | 68 | 3
No Worker required to work inside the Manhole
* Risk of fall of person mitigated by immediate placing of M S Grill on opening.

## Slide 16
ISSUES WITH DIFFERENT TYPES OF MANHOLES
The chockage of Sewer lines are cleared through downstream manhole. Cleaning can only be ensured from the areas marked with This requires manual entry for access
Point of manual entry
Point of manual entry
Point of manual entry

## Slide 17
To further aid the cleaning mechanism 3 Nos opening were provided in T shape & 2 Nos in L Shape, after dismantling and recasting of manhole top slab
CHANGE IN DESIGN OF EXISTING MANHOLES
Point of manual entry
AFTER
BEFORE
Point of manual entry
point of machine pipe entry

## Slide 18
Conversion of L & T Type Manhole
BEFORE
AFTER
AFTER

## Slide 19
MANUAL METHOD OF SEWER PIPE CLEANING
MH
MH
SEWER PIPE
SILT
SILT
MECHANIZED CLEANING OF SEWER PIPE USING POWER BUCKET
THEN
NOW

## Slide 20: Mechanization Journey under SmSC
Formation of Responsible Sanitation Authority (RSA), Sanitation Response Unit (SRU)
Establishment of Call Centre
Establishment of Safety Training Centre
For handling of mechanized equipment special training to SafaiMitras
Public sensitization on safety measures
Purchase of Mechanized Equipment
Ban on Manual Scavenging

## Slide 21: promoting Safety, Dignity and Social Security
Daily Tool Box Talk
Mandatory PPE uses
Mandatory Safety Training
Converting Manhole to Machine Hole
Geo-Tagging of all the septic tanks
Daily Tool Box Talk
Mandatory Safety Training
Converting Manhole to Machine Hole

## Slide 22
Feast for SafaiMitras
promoting Safety, Dignity and Social Security
Recognition of Best Workers on monthly basis
Regular Health Checkup Camps for SafaiMitras

## Slide 23
Capacity Building and Welfare Measures for SafaiMitras
Linkage to Social Welfare Schemes
Regular Mass Meeting
Linkage with PM Jivan Jyoti Bima
Regular Health Check-up Camp

## Slide 24
Practices : Connecting with the Family Members

## Slide 25: “Citizen Connects” to Spread Awareness for Safety of SafaiMitras
More safety to SafaiMitras
Strategic IEC outreach
Customer contact program in every 2 months in each locality
Two app's of TSUISL are used i.e Zimmedaar Nagrik and JUSCO Sahyog as customer support

## Slide 26
Monitoring of workmen entry
We achieved “ZERO” workmen entry for manhole cleaning
From 1st January 2021
Chart: % Elimination of Manual entry in Manhole < 2m depth
| 44166 | 44197 | 44228 | 44256
% Elimination | 55.0369 | 100 | 100 | 100
Chart: % Elimination of Manual Scavenging Manhole Depth >2 mtr.
| 43739 | 43770 | 43800 | 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075 | 44105 | 44136 | 44166 | 44197 | 44228 | 44256
% Elimination | 5.45 | 18.66 | 33.33 | 80 | 51.82 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
Phase 1
Phase 2
OTHER BENEFITS
Customer KPI | FY-19 | FY-20 | FY-21 | FY-22
Compliance within SLG | 94% | 95% | 95% | 98%
Customer Satisfaction performance score for Waste water services | 89% | 90% | 94% | 95%

## Slide 27: TESTIMONIAL
For SafaiMitras
Man hole worker to a mechanized sewer worker
No Life at Risk
Better working condition
Social Security- Linked with schemes
Recognition- Working with Dignity
Uplifted SafaiMitras for a better and healthy life
Safety
Dignity
Social Security
Name: Mr. Baset Hasda
Occupation: Sewer Worker Working Zone: West
City: Jamshedpur State: Jharkhand

## Slide 28
SAFAIMITRAS are the backbone of the
City, they are our Responsibility:
Some Sewer Operators & Sewer Men feeling dignified…
Thank You
Vinod Jha Atisher Bhumiz Aazadi Bagti Kuna Hembrom